SolarKeymark-II

Large open EU market for solar thermal products

Deliverable D 18

Energy Performance Certificate: Contribution of solar thermal systems

Dominique CACCAVELLI – Carol BUSCARLET  (CSTB)

Project co-ordination: ESTIF

10th, December 2007

This project is co-funded by the European Community

Contract n° EIE/05/052/SI2.420194

CONTENT

1	INTRODUCTION	3

2	METHODOLOGY	4

3	RESULTS	5

3.1	Two storey detached house	5

3.2	One storey detached house	6

3.3	Two storey terraced house	7

3.4	Apartment building	10

4	CONCLUSION	12

# INTRODUCTION

The Energy Performance Building Directive (EPBD) prescribes the use of an Energy Performance Certificate (EPC). This EPC displays the energy performance of a building and cost-effective measures to enhance energy performance are advised. Detailed implementation is left to the Member States, thus allowing each MS to choose the regime that corresponds best to its particular situation.

From 2006, when a dwelling is built, sold or rented out, an Energy Performance Certificate should be supplied mandatory.

The energy performance of buildings should be calculated on the basis of a methodology, which may be differentiated at regional level. The methodology should include aspects concerning:

- thermal characteristics

- installation (heating, hot water supply, air conditioning)

- application of renewable energy sources

- natural ventilation

- passive solar systems and solar protection

- indoor climatic conditions.

A survey performed during the frame of the Solarkeymark II project (D17) has shown that most of MS already have softwares or methods enabling to assess the energy performance of a building. If the majority of these methods are well adapted to new buildings, only some of them are adapted to existing buildings. Furthermore, only few countries have integrated solar thermal systems into their calculation methods.

The EN 15316-4.3 standard allows to calculate the contribution of thermal solar system to space heating and/or domestic hot water needs and the thermal losses and auxiliary energy consumption of the thermal solar system. Because this standard was only adopted in June 2007, it has not been implemented in any existing softwares enabling to assess the energy performance of a building so far.

A software (SOLEN), based on EN 15316-4.3 standard, has been developed in the framework of the European SolarKeymark II project. This software allows calculating the monthly and annual thermal performance of a solar thermal system as well as the energy savings and the quantity of CO2 avoided compared with a conventional system.

This report aims at demonstrating how software based on EN 15316-4.3 standard can be used in conjunction with energy performance calculation methods and how Energy Performance Certificate can be positively influenced by solar thermal systems.

# METHODOLOGY

We used the following methodology to assess the impact of solar thermal systems on EPC (see Figure 1):

- selection of typical residential buildings (both dwellings and apartment buildings);

- selection of an energy performance calculation method. We used the 3CL French method developed by the Tribu Energie consulting company;

- for each typical residential building, an energy performance assessment is performed and an EPC is issued;

- different solar thermal systems (SDHW, comby system) are simulated for different climates using the SOLEN software and the impact of these systems on the reduction of the total energy consumption of the building is calculated;

- a new EPC is issued taking into account the contribution of thermal solar systems to space heating and/or domestic hot water needs.

Figure 1 – Methodology – Step to step

# RESULTS

## Two storey detached house

This typical two storey residential house is located in the Paris suburb. The house was built in 1989. Heated area is 85 m². Figures 2 and 3 show the front elevation and plan of the house.

Figure 2 – Two storey detached house – Front elevation

Figure 3 – Two storey detached house – Plan

Concerning the initial configuration of the heating system (called reference system), 2 case studies were performed:

- Both space heating and domestic hot water production are operated using a gas-fired boiler.

- Space heating is operated using electrical appliances and domestic hot water is produced with an electric water heater.

A Solar Domestic Hot water system with 3 m² of solar collector was considered to enhance energy performance of the house.

Tables 1 and 2 show the main results for the 2 configurations. Results are expressed in kWh per year (of primary energy) and in kWh per m² of heated area and per year.

| Heating system | Heating | DHW | Solar | Total | Energy efficiency |
| --- | --- | --- | --- | --- | --- |
|  | kWh(PE) | kWh(PE) | Fraction | kWh (PE)/m² | class |
| Reference system | 11269 | 2505 | 0% | 162 | D |
| Solar water heater | 11269 | 1137 | 61% | 146 | C |
| Gain |  |  |  | -10% |  |

Table 1 – Two storey detached house - Gas heating

| Heating system | Heating | DHW | Solar | Total | Energy efficiency |
| --- | --- | --- | --- | --- | --- |
|  | kWh(PE) | kWh(PE) | Fraction | kWh (PE)/m² | class |
| Reference system | 17148 | 6223 | 0% | 275 | E |
| Solar1 water heater | 17148 | 2587 | 61% | 232 | E |
| Gain |  |  |  | -16% |  |

Table 2 – Two storey detached house - Electric heating

## One storey detached house

This typical one storey residential house is located in the Alpin mountain region near Lyon. The house was built in 1993. Heated area is 100 m². Figure 4 shows a plan of the house.

Concerning the initial configuration of the heating system (called reference system), only one option was investigated: space heating and domestic hot water production are operated using a gas-fired boiler.

A Solar Combi System (both space heating and domestic hot water production) with 12 m² of solar collector was the only cost-effective measure considered to enhance energy performance of the house.

Figure 4 – One storey detached house – Plan

Table 3 shows the main results of the study. Results are expressed in kWh per year (of primary energy) and in kWh per m² of heated area and per year.

| Heating system | Heating | DHW | Solar | Total | Energy efficiency |
| --- | --- | --- | --- | --- | --- |
|  | kWh(PE) | kWh(PE) | Fraction | kWh (PE)/m² | class |
| Reference system | 11269 | 2505 | 0% | 138 | D |
| Solar Combi system | 8378 | 41% | 84 | B |
| Gain |  |  |  | -39% |  |

Table 3 – One storey detached house - Gas heating

## Two storey terraced house

This typical two storey terraced house is located in the South part of France near Cannes. The house was built in 1992. Heated area is 159 m². Figures 5 and 6 show the front elevation and plan of the house.

Concerning the initial configuration of the heating system (called reference system), only one option was investigated: space heating is operated using an oil-fired boiler and domestic hot water is produced with an electric water heater.

A Solar Domestic Hot Water system with 3 m² of solar collector was the only cost-effective measure considered to enhance energy performance of the house.

Figure 5 – Two storey terraced house – Front elevation

Figure 6 – Two storey terraced house – Plan

Table 4 shows the main results of the study. Results are expressed in kWh per year (of primary energy) and in kWh per m² of heated area and per year.

| Heating system | Heating | DHW | Solar | Total | Energy efficiency |
| --- | --- | --- | --- | --- | --- |
|  | kWh(PE) | kWh(PE) | Fraction | kWh (PE)/m² | class |
| Reference system | 11093 | 6938 | 0% | 113 | C |
| Solar 1 water heater | 11093 | 1270 | 84% | 78 | B |
| Gain |  |  |  | -31% |  |

Table 4 – Two storey terraced house

## Apartment building

This typical apartment, located in the Paris city, is positioned at the second floor of a multi storey building. The building was built in 2000. Heated area of the flat is 66 m². Figure 7 shows a plan of the flat.

Concerning the initial configuration of the heating system (called reference system), only one option was investigated: space heating and domestic hot water are produced using a central gas-fired boiler.

A solar thermal installation for the production of Domestic Hot Water with 1.5 m² of solar collector per flat was the only cost-effective measure considered to enhance energy performance of the building.

Figure 7 – Apartment building – Plan

Table 5 shows the main results of the study. Results are expressed in kWh per year (of primary energy) and in kWh per m² of heated area and per year.

| Heating system | Heating | DHW | Solar | Total | Energy efficiency |
| --- | --- | --- | --- | --- | --- |
|  | kWh(PE) | kWh(PE) | Fraction | kWh (PE)/m² | class |
| Reference system | 5950 | 3419 | 0% | 142 | C |
| Solar installation | 5950 | 1880 | 45% | 119 | C |
| Gain |  |  |  | -16% |  |

Table 5 – Apartment building

# CONCLUSION

Energy Performance Certificate is mandatory when a house or an apartment is built, sold or rented out. Together with this EPC, experts should advise the owner with cost-effective measures to enhance energy performance of the building. It is expected that this will have a major impact on the increased awareness of building owners and users regarding the energy performance of buildings. It will probably play a key role in the improvement of existing buildings that is a major challenge in reducing building CO2 emissions.

Up to mid 2007, the impact of solar thermal energy in these certification procedures was weak due to the lack of harmonized calculation methods. With the adoption in June 2007 of EN 15316-4.3 standard it can be expected that solar thermal energy will play an increased role in the refurbishment of building as an efficient energy-saving measure.

This report has shown that the installation of solar thermal systems in existing buildings (both dwelling and flat) can have a rather strong impact on the ranking of building energy performance in terms of energy-efficient class.

# Footnotes

The backup system for the Solar Domestic Hot Water system uses the same energy as the reference system.

The backup system for the Solar Combi system uses the same energy as the reference system.